## Slide 1
Influence of different substrates on the polarization effect of InGaN-based LEDs
Li Liu，Qingqing Feng，Wenxiao Wu，Chao Zeng，Zhihua Xiong*
The 3rd International Conference on Applied Mathematics,
Modeling and Computer Simulation (AMMCS 2023)
Key Laboratory for Optoelectronics and Communication of Jiangxi Province
https://jxgd.jxstnu.edu.cn

## Slide 2
InGaN-based LEDs ( Green /Red / Blue )
Research background
EQE (external quantum efficiency)
Blue 80%
Green 40%
Red < 2.5%
AR/VR
MAC Large Screen Display
Garmin HUD
The EQE of InGaN-based yellow LEDs/Substrate
13.4% /semi-polar GaN
18.9% /c-faced sapphire
33.7% /Si
Quantum confinement Stark effect (QCSE)
induced by lattice mismatch
This is a challenge:
The efficiency of long wavelength LED decreases

## Slide 3
“The interface is the device”
---- Prof. Herbert Kroemer
LEDs diagram
Theory background
Lattice mismatch
between substrate and GaN
The compression strain of InGaN well layer
decrease
The strain state of GaN
Compressive: Sappphire and SiC Tensile: Si
Polarization field induced QCSE decrease

## Slide 4
Computational process
Calculate model
Calculate method
Density functional theory (DFT)
based on Ab into calculation
Electron kinetic energy
The potential energy of electrons and nuclei (electrons)
The exchange-correlation energy among electrons
GaN/In0.3Ga0.7N/GaN supercell
Generalized Gradient Approximation (GGA)
Perdew-Berke-Ernzerhof (PBE)
GaN
GaN
InGaN

## Slide 5
Calculation result
Band decomposed charge density
belonging to CBM/VBM at Γ point
VBO reduction facilitates hole injection
into InGaN/GaN QWs

## Slide 6
Calculation result
The internal piezoelectric field of InGaN layer decreases with decreasing compressive strain.
The piezoelectric polarization results in the separation of positive and negative charge centers.

## Slide 7
Calculation result
The compressive strain of InGaN layer decrease
The piezoelectric polarization decrease
The polarized bound charge decrease
The recombination of electrons and holes in QWs is enhanced

## Slide 8: Thank you for listening!
The 3rd International Conference on Applied Mathematics,
Modeling and Computer Simulation (AMMCS 2023)
Influence of different substrates on the polarization effect of InGaN-based LEDs
Reporter: Liuli